## Slide 1: Fuel Supply Chain Model
James Robinson and Steven Witkin

## Slide 2: Overall Structure
Input
Input is read from a 5-sheet Excel workbook
Modeling
The python code uses Pyomo for model construction and Gurobi for solving.
Output
Output is saved in a formatted Excel spreadsheet

## Slide 3: Input
Input is classified into five classes:
  Sources
  Sinks
  Transformers
  Connectors
  Hubs
Each instance of each class has a flexible number of inputs

## Slide 4: Input
Input is read from the spreadsheet using Pandas
Lists of each class are constructed, containing all objects of that class
This should be able to handle any number of each kind of component, as long as input format is correct
CO2 restriction must be modified in the source code, not the input file

## Slide 5: Model Construction
Pyomo uses the component lists to construct a linear or non-linear model
While flexible, if new types of data are added to an existing component, or if new components are added, some minor changes will need to be made
Gurobi is currently used as the model solver, but this is easily changeable

## Slide 6: Output
Output is automatically sent to a spreadsheet
For each fuel type used in the test, MJ by fuel and total system cost are listed
Cost by fuel and CO2 by fuel are not currently implemented, but could be in the future